## Slide 1
Specifications
Copyright © 2015 EVE Energy Company . All Rights Reserved.
EVE C40
For more details, please contact: EVE Energy North America, 46 Village Pointe Dr, Powell, Ohio, 43065
Email: info@evebatteryusa.com Phone: 614.389.2552
Dimensions (mm)
Item | Standards | Remarks
Nominal Capacity | 20.5Ah | 0.33C, 25±2oC, 2.5~3.65V
Nominal Energy | 19.5Ah | 0.33C, 25±2oC, 2.5~3.65V
Initial IR | ≤2mΩ | AC, 1kHz, 30% SOC
Nominal Voltage | 3.25V | 
Weight | 374g | Max
Charging Cut-off Voltage | 3.65V | 
Discharging Cut-off Voltage | 2.5V (T>0oC) 2.0V (T≤0oC) | 
Max Cont. Charging Current | 20A | 1C
Max Cont. Discharging Current | 60A | 3C
Cycling Performance | 4000 cycles (25oC) 1500 cycles (45oC) | 
Operation Temperature | Charging (0~50oC) Discharging (-20~60oC) | 
Storage Temperature | 3 month (0~45oC) 1 month (-20~45oC) | 
Lithium Iron Phosphate Cell